## Slide 1: Project Status Report
Presentation By,
Prajna R
Ramya V.R
Department of ISE
PESIT
Bangalore
Internal Guide ,
Dr. Mamatha HR
Professor
Department of ISE
PESIT
Bangalore
TEXT LINE EXTRACTION FROM PRINTED KANNADA DOCUMENTS
Notes: This template can be used as a starter file to give updates for project milestones.
Sections
Right-click on a slide to add sections. Sections can help to organize your slides or facilitate collaboration between multiple authors.
Notes
Use the Notes section for delivery notes or to provide additional details for the audience. View these notes in Presentation View during your presentation.
Keep in mind the font size (important for accessibility, visibility, videotaping, and online production)
Coordinated colors
Pay particular attention to the graphs, charts, and text boxes.
Consider that attendees will print in black and white or grayscale. Run a test print to make sure your colors work when printed in pure black and white and grayscale.
Graphics, tables, and graphs
Keep it simple: If possible, use consistent, non-distracting styles and colors.
Label all graphs and tables.

## Slide 2: Agenda
Introduction
Problem Definition
Motivation
Literature Survey
About Data Set
Method Explanation
Comparative Study
Conclusion
Future Enhancements

## Slide 3: Introduction
An Optical Character Recognition (OCR) system is the process of transforming human readable and optically sensed data to machine understandable codes.
OCR system has the following steps :
OCR System
Image Acquisition
Pre-processing
Segmentation
Feature Extraction
Classification and Recognition

## Slide 4: Problem Definition
Segmentation is an important task of any Optical Character Recognition (OCR) system.
Segmentation is the process of extracting objects of interest from an image.
“Text line extraction from printed Kannada documents” is the first step in segmentation process.
For the extraction of lines we have implemented three segmentation methodologies.

## Slide 5: Motivation
Efficient OCR systems for Kannada are one of the present day requirements.
Line segmentation is very important for further process.
Not many works are reported for Printed Kannada documents.
Notes: Sunny Buffalo university

## Slide 6: Characteristics Of Kannada Script Includes 16 vowels and 35 consonants Vowels in Kannada script Consonants in Kannada script

## Slide 7: Consonant-vowel composite characters of first consonant Conjunct Consonant (Subscript/Vatthu)

## Slide 8: Text Line Components
Baseline: fictitious line which follows and joins the lower part of the character bodies in a text line .
Upper line: fictitious line which joins the top of ascenders.
Lower line: fictitious line which joins the bottom of descenders.

## Slide 9: Literature Survey
Author | Name Of the Paper | Method Used For Text Line Segmentation | Accuracy
R Sanjeev Kunte and R D Sudakher Samuel | An OCR system for printed Kannada text using Two-stage Multi-network classification approach employing Wavelet features | Horizontal Projection | 92%
Mamatha H R and Srikantamurthy K | Morphological Operations and Projection Profiles based Segmentation of Handwritten Kannada Document | Morphological Operations and Projection Profiles | 94.5%

## Slide 10: Data Set
Data set is generated through Baraha software.
Single column documents are considered for line extraction.
Different documents with different font style and different font sizes are considered for extraction of lines.
Documents contains lines in range 14-24.

## Slide 11: Sample Documents Original Image with font style BRHKannada and font size 22

## Slide 12: Original Image with font style BRHAmerikannda and font size 16

## Slide 13: Original Image with font style BRHBenguluru and font size18

## Slide 14: Original image with font style BRHkailasm and font size 18

## Slide 15: Original Image with font style BRHKannadaRN and font size 7

## Slide 16: Original Image with font style BRHSrigandha and size 14

## Slide 17: Original Image with font style BRHVijay and size 16

## Slide 18: System Design

## Slide 19: Data Flow Diagram
Preprocessing
Segmentation

## Slide 20: Preprocessing
Gray Scale Conversion
a grayscale image is an image in which the value of each pixel is a single sample, that is, it carries only intensity information.

## Slide 21
Binarization
Image binarization converts an image to a black and white image. Frequently, binarization is used as a pre-processor before OCR.
The simplest way to use image binarization is to choose a threshold value, and classify all pixels with values above this threshold as white, and all other pixels as black.

## Slide 22: Example
Original Image Gray scale Binary

## Slide 23: Original Image

## Slide 24: Gray Scale and Binary Image

## Slide 25: Horizontal Projection Profile
Data Flow Diagram:
PREPROCESSING
PROJECTION
TECHNIQUE
& EXTRACTION

## Slide 26: Algorithm
Algorithm
Begin
Input: Printed Kannada text document
Output: Segmented lines
Method:
Step 1: Binarize the original image.
Step 2: Find the minimum and maximum positions of the zero valued
pixels to identify the rows. Step 3: Horizontal projection is applied for line segmentation
End

## Slide 27: Horizontal Projection Profile Boundary line

## Slide 28: Original Image with font style BRH Amerikannada and font size 16

## Slide 29: Gray Scale and Binary image

## Slide 30: Detected and Extracted line

## Slide 31: Original Image with font style BRH Kannada & font size 22 and extracted line

## Slide 32: Morphology Based Approach
Data Flow Diagram:
PREPROCESSING
MORPHOLOGY
OPERATIONS
PROJECTION AND
EXTRACTION

## Slide 33: Image Morphology
Morphology is a tool for extracting image components that are useful in the representation and description of region shape, such as boundaries and skeletons.
Two basic Morphology operations:
Dilation: primitive morphological operation that grows or thickens objects in a binary image
Erosion: shrinks or thins objects in a binary image

## Slide 34: Example Binary Image Erosion Dilation

## Slide 35: Erode and Dilated Image

## Slide 36: Algorithm
Algorithm
Begin
Input: Printed Kannada text document
Output: Segmented lines
Method:
Step 1: Binarize the original image.
Step 2: Erosion followed by dilation operations are applied
Step 3: find the minimum and maximum positions of the zero valued
pixels to identify the rows
Step 4: Horizontal projection is applied for line segmentation
End

## Slide 37: Original Image with font style BRH Kannada and font size 25

## Slide 38: Grayscale Image

## Slide 39: Binary image

## Slide 40: Eroded and Dilated image

## Slide 41: Detected and Extracted line

## Slide 42: Original Image with font style BRH kailasam,fontsize 20 and Extracted line

## Slide 43: Bounding Box Approach Data flow diagram:
PREPROCESSING
BOUNDING BOX
TECHNIQUE
& EXTRACTION

## Slide 44: Algorithm
Algorithm
Begin
Input: Printed Kannada text document
Output: Segmented lines
Method:
Step 1: Convert the original image to gray scale.
Step 2: Histogram is plotted and white spaces are found
Step 3: find centroids of white gaps
Step 4: Measurements of centroids is found using regionprops and
lines are cropped using the measurements of centroids
End

## Slide 45: Original Image with font style BRH Amerikannada and font size 26

## Slide 46: Binary image and Extracted line

## Slide 47: Original Image with font style BRH Srigandha, font size 25 and Extracted Line

## Slide 48: Comparative Study
Author | Segmentation Method | Size of dataset | Segmentation rate (%)
R Sanjeev Kunte et al.,[7] | Horizontal Projection based approach | 20 | 92
Proposed Method 1 | Horizontal Projection based approach | 35 | 84
Proposed Method 2 | Morphological operations and projection profile based approach | 35 | 86
Proposed Method 3 | Bounding Box based approach | 35 | 80

## Slide 49: Conclusion
Accuracy obtained from the proposed method is reduced because we have considered different documents with different font sizes such as 15,25,28 and different font styles such as kailasam,vijaya etc.
If the accuracy of line segmentation is less than the accuracy of word and character segmentation reduces,eventually the extracted characters will be misinterpreted in OCR.

## Slide 50: Future Enhancements
Use of double column documents
Single document with different font styles and font sizes
Word and character extraction

## Slide 51: References
[1] Nallapareddy Priyanka, Srikanta Pal, Ranju Mandal “Line and Word Segmentation Approach for Printed Documents”, IJCA Special Issue on “Recent Trends in Image Processing and Pattern Recognition”RTIPPR, 2010.
[2] Sunanda dixit,Suresh Hosahalli Narayana,Mahesh Belur “Kannada text line extraction based on energy minimization and skew correction”.
[3] B. Gangamma, Srikanta Murthy K, Riddhi J. Shah, Swati D V “Text Line Extraction from Palm Script Documents Using Morphological Approach”
[4] Vikas J Dongre , Vijay H Mankar “Devnagari document segmentation using histogram approach”.International Journal of Computer Science, Engineering and Information Technology (IJCSEIT), Vol.1, No.3, August 2011
[5] Alireza Alaei, P. Nagabhushan, Umapada Pal “A Benchmark Kannada Handwritten Document Dataset and its Segmentation” 2011 International Conference on Document Analysis and Recognition.

## Slide 52
[6] U. Pal and B. B. Chaudhuri “Script Line Separation From Indian Multi-Script Documents”.In Proc. 4thICDAR.
[7] R. Sanjeev Kunte, R. D. Sudhaker Samuel An OCR system for printed Kannada text using Two-stage Multi-network classification approach employing Wavelet features”,International Conference on Computational Intelligence and Multimedia Applications 2007.
[8] Mamatha Hosalli Ramappa and Srikantamurthy Krishnamurthy “Skew Detection, Correction and Segmentation of Handwritten Kannada Document”,International Journal of Advanced Science and Technology Vol. 48, November, 2012.
[9] M.RaviKumar, R.Pradeep,B.S.PuneethKumar,Prasad Babu“A Simple Text-line segmentation Method for Handwritten Documents”, IJCA Proceedings on National Conference on Advanced Computing and Communications 2012NCACC(1):46-61, August 2012.
[10] G. Louloudi1, B. Gatos, I. Pratikakis, C. Halatsis. “Line And Word Segmentation of HandwrittenDocuments”,Proceedings of the1st International Conference on Frontiers in Handwriting Recognition (ICFHR), 247-252.

## Slide 53
[11]M.Ravi Kumar, R. Pradeep, B.S.PuneethKumar,PrasadBabu“A Simple Text-line segmentation Method for Handwritten Documents”, IJCA Proceedings on National Conferecne on Advanced Computing and Communications 2012NCACC(1):46-61, August 2012.
[12] Mamatha H R, Srikantamurthy K “Morphological Operations and Projection Profiles based Segmentation of Handwritten Kannada Document” International Journal of Applied Information Systems (IJAIS) – ISSN : 2249-0868 Foundation of Computer Science FCS, New York, USA Volume 4– No.5,October 2012 – www.ijais.org

## Slide 54: Paper Work
Based on the work done for the project,we have written paper named- A Study of different Text Line Extraction Techniques for Multi-font and Multi-size Printed Kannada Documents.
Uploaded to IJCA(International Journal of Computer Applications) june 2015